## Slide 1
Scientific and Engineering Notation
© 2014 Project Lead The Way, Inc.
Digital Electronics

## Slide 2: Scientific & Engineering Notation
This presentation will demonstrate…
How to express numbers in scientific notation.
How to express numbers in engineering notation.
How to express numbers in SI prefix notation.

## Slide 3: Scientific Notation
Scientific notation is a way of writing very large and very small numbers in a compact form.
A number written in scientific notation is written in the form:
  a × 10b
  Where: a is a number greater than 1 and less than 10
    b is an integer
    Examples:
    3.24 × 105
    1.435 × 10-7
    3.29× 106
    7.3 × 10−2

## Slide 4: Writing A Number in Scientific Notation
Shift the decimal point so that there is one digit (which cannot be zero) before the decimal point.
Multiply by a power of 10, equal to the number of places the decimal point has been moved.
The power of 10 is positive if the decimal point is moved to the left and negative if the decimal point is moved to the right.

## Slide 5: Scientific Notation: Example #1
Example:
  Express 5630 in scientific notation.
5
  5.63 × 103

## Slide 6: Scientific Notation: Example #2
Example:
  Express 0.000628 in scientific notation.
6
  6.28 × 10−4

## Slide 7: Engineering Notation
Engineering notation is similar to scientific notation. In engineering notation the powers of ten are always multiples of 3.
A number written in engineering notation is written in the form:
  a × 10b
  Where: a is a number greater than 0 and less than 999
    b is an integer multiple of three
    Examples:
    71.24 × 103
  4.32 × 10-6
  320.49 × 109
  123.452 × 10−12

## Slide 8: Writing A Number in Engineering Notation
Shift the decimal point in “groups of three” until the number before the decimal point is between 0 and 999.
Multiply by a power of 10 that is equal to the number of places the decimal point has been moved.
The power of 10 is positive if the decimal point is moved to the left and negative if the decimal point is moved to the right.

## Slide 9: Engineering Notation: Example #1
Example:
  Express 16346000000 in engineering notation.
9
  16.346 × 10−9

## Slide 10: Engineering Notation: Example #2
Example:
  Express 0.0003486 in engineering notation.
10
  348.6 × 10−6

## Slide 11: SI Prefixes
SI prefixes are a shorthand way of writing engineering notation for SI numbers.
The International System of Units (abbreviated SI from the French Système International d'Unités) is the modern form of the metric system. It is the world's most widely used system of units for science and engineering.

## Slide 12: Commonly Used SI Prefixes
Value | Prefix | Symbol
1012 | tera | T
109 | giga | G
106 | mega | M
103 | kilo | k
10-3 | milli | m
10-6 | micro | 
10-9 | nano | n
10-12 | pico | p
10-15 | femto | f

## Slide 13: SI Notation: Example #1
Example:
  Express 27500  using standard SI notation.
  (Note:  is the Greek letter omega. In electronics, it is the symbol used for resistance.)
13
  27.5 × 103 
  27.5 m

## Slide 14: SI Notation: Example #2
Example:
  Express 0.000568 Volts using standard SI notation.
14
  568 × 10-6
  568 μ

## Slide 15: Common Electronic Symbol & Units
Quantity | Symbol | Unit
Current | I | Ampere (A)
Voltage | V | Volt (V)
Resistance | R | Ohm ()
Frequency | ƒ | Hertz (Hz)
Capacitance | C | Farad (F)
Inductance | L | Henry (H)
Power | P | Watt (W)