## Slide 1
Circuit Theory Laws
© 2014 Project Lead The Way, Inc.
Digital Electronics

## Slide 2: Circuit Theory Laws
This presentation will
Review voltage, current, and resistance.
Review and apply Ohm’s Law.
Review series circuits.
  Current in a series circuit
  Resistance in a series circuit
  Voltage in a series circuit
Review and apply Kirchhoff’s Voltage Law.
Review parallel circuits.
  Current in a parallel circuit
  Resistance in a parallel circuit
  Voltage in a parallel circuit
Review and apply Kirchhoff’s Current Law.
Notes: Introductory Slide / Overview of Presentation

## Slide 3: Electricity – The Basics
An understanding of the basics of electricity requires the understanding of three fundamental concepts.
Voltage
Current
Resistance
A direct mathematical relationship exists between voltage, resistance, and current in all electronic circuits.
Notes: Introduction to the three basic elements of electricity/electronics

## Slide 4: Voltage, Current, & Resistance
Andre Ampere
1775-1836
French Physicist
Current – Current is the flow of electrical charge through an electronic circuit. The direction of a current is opposite to the direction of electron flow. Current is measured in AMPERES (AMPS).
Notes: The formal definition of current and the scientist that bears their name.
http://commons.wikimedia.org/wiki/Image:Andre-marie-ampere2.jpg

## Slide 5: Voltage
Alessandro Volta
1745-1827
Italian Physicist
Voltage – Voltage is the electrical force that causes current to flow in a circuit. It is measured in VOLTS.
Notes: The formal definition of voltage and the scientist that bears their name.
http://commons.wikimedia.org/wiki/Image:Alessandro_volta2.jpg

## Slide 6: Resistance
Georg Simon Ohm
1789-1854
German Physicist
Resistance – Resistance is a measure of opposition to current flow. It is measured in Ohms.
Notes: The formal definition of resistance and the scientist that bears their name.
http://commons.wikimedia.org/wiki/Image:Ohm3.gif

## Slide 7: First, An Analogy
Force
The flow of water from one tank to another is a good analogy for an electrical circuit and the mathematical relationship between voltage, resistance, and current.
Force: The difference in the water levels ≡ Voltage
Flow: The flow of the water between the tanks ≡ Current
Opposition: The valve that limits the amount of water ≡ Resistance
Flow
Opposition
Notes: The classic water analogy for voltage/current/resistance.

## Slide 8: Anatomy of a Flashlight
- +
D - Cell
Switch
Switch
Light
Bulb
Light
Bulb
Battery
Battery
Block Diagram
Schematic Diagram
Notes: This slide shows an everyday object (flashlight), its block diagram, and the equivalent schematic.
http://commons.wikimedia.org/wiki/Image:Flashlight_450x190_commons.jpg

## Slide 9: Flashlight Schematic
Closed circuit (switch closed)
Current flow
Lamp is on
Lamp is resistance, uses energy to produce light (and heat)
Open circuit (switch open)
No current flow
Lamp is off
Lamp is resistance, but is not using any energy
- +
- +
Current
Voltage
Resistance
Notes: This slide shows the flow of electrons (not really; it’s the flow of current . . . see the next slide) when the switch closed.

## Slide 10: Current Flow
Conventional Current assumes that current flows out of the positive side of the battery, through the circuit, and back to the negative side of the battery. This was the convention established when electricity was first discovered, but it is incorrect!
Electron Flow is what actually happens. The electrons flow out of the negative side of the battery, through the circuit, and back to the positive side of the battery.
Electron
Flow
Conventional
Current
Notes: Conventional Current vs. Electron Flow (Scientists vs. Engineers – since this is an engineering course, guess who wins?).

## Slide 11: Engineering vs. Science
The direction that the current flows does not affect what the current is doing; thus, it doesn’t make any difference which convention is used as long as you are consistent.
Both Conventional Current and Electron Flow are used. In general, the science disciplines use Electron Flow, whereas the engineering disciplines use Conventional Current.
Since this is an engineering course, we will use Conventional Current.
Electron
Flow
Conventional
Current
Notes: Of course, the engineers win!

## Slide 12: Ohm’s Law
Defines the relationship between voltage, current, and resistance in an electric circuit
Ohm’s Law:
    Current in a resistor varies in direct proportion to the voltage applied to it and is inversely proportional to the resistor’s value.
Stated mathematically:
  Where: I is the current (amperes)
  V is the potential difference (volts)
  R is the resistance (ohms)
V
I
R
+ -
Notes: Introduction to Ohm’s Law

## Slide 13: Ohm’s Law Triangle
V
I
R
V
I
R
V
I
R
Notes: Ohm’s Law Triangle – Place your finger over the unknown quantity and what remains is the equation used to solve for the unknown.

## Slide 14: Example: Ohm’s Law
Example:
  The flashlight shown uses a 6 volt battery and has a bulb with a resistance of 150 . When the flashlight is on, how much current will be drawn from the battery?
Notes: Pause the presentation and allow the student to work on the example. The solution is on the next slide.

## Slide 15: Example: Ohm’s Law
Example:
  The flashlight shown uses a 6 volt battery and has a bulb with a resistance of 150 . When the flashlight is on, how much current will be drawn from the battery?
Solution:
VT =
+
-
VR
IR
Schematic Diagram
V
I
R
Notes: This slide provides the solution. If you print handouts, do not print this page.

## Slide 16: Circuit Configuration
Series Circuits
Components are connected end-to-end.
There is only a single path for current to flow.
Parallel Circuits
Both ends of the components are connected together.
There are multiple paths for current to flow.
Components
(i.e., resistors, batteries, capacitors, etc.)
Components in a circuit can be connected in one of two ways.
Notes: Overview of series and parallel component configuration.

## Slide 17: Series Circuits
Characteristics of a series circuit
The current flowing through every series component is equal.
The total resistance (RT) is equal to the sum of all of the resistances (i.e., R1 + R2 + R3).
The sum of all of the voltage drops (VR1 + VR2 + VR2) is equal to the total applied voltage (VT). This is called Kirchhoff’s Voltage Law.
VT
+
-
VR2
+
-
VR1
+
-
VR3
+
-
RT
IT
Notes: Characteristics of a series circuit.

## Slide 18: Example: Series Circuit
Example:
  For the series circuit shown, use the laws of circuit theory to calculate the following:
    The total resistance (RT)
    The current flowing through each component (IT, IR1, IR2, and IR3)
    The voltage across each component (VT, VR1, VR2, and VR3)
    Use the results to verify Kirchhoff’s Voltage Law.
VT
+
-
VR2
+
-
VR1
+
-
VR3
+
-
RT
IT
IR1
IR3
IR2
Notes: Pause the presentation and allow the student to work on the example. The solution is on the next three slides.

## Slide 19: Example: Series Circuit
Solution:
V
I
R
Total Resistance:
Current Through Each Component:
Notes: This slide provides the solution. If you print handouts, don’t print this page. (1 of 3)

## Slide 20: Example: Series Circuit
Solution:
Voltage Across Each Component:
V
I
R
Notes: This slide provides the solution. If you print handouts, don’t print this page. (2 of 3)

## Slide 21: Example: Series Circuit
Solution:
Verify Kirchhoff’s Voltage Law:
Notes: This slide provides the solution. If you print handouts, don’t print this page. (3 of 3)

## Slide 22: Parallel Circuits
Characteristics of a Parallel Circuit
The voltage across every parallel component is equal.
The total resistance (RT) is equal to the reciprocal of the sum of the reciprocal:
The sum of all of the currents in each branch (IR1 + IR2 + IR3) is equal to the total current (IT). This is called Kirchhoff’s Current Law.
+
-
+
-
VR1
+
-
VR2
VR3
RT
VT
IT
+
-
Notes: Characteristics of a parallel circuit.

## Slide 23: Example: Parallel Circuit
Example:
  For the parallel circuit shown, use the laws of circuit theory to calculate the following:
    The total resistance (RT)
    The voltage across each component (VT, VR1, VR2, and VR3)
    The current flowing through each component (IT, IR1, IR2, and IR3)
    Use the results to verify Kirchhoff’s Current Law.
23
+
-
+
-
VR1
+
-
VR2
VR3
RT
VT
IT
+
-
IR1
IR2
IR3
Notes: Pause the presentation and allow the student to work on the example. The solution is on the next three slides.

## Slide 24: Example: Parallel Circuit
Solution:
Total Resistance:
Voltage Across Each Component:
Notes: This slide provides the solution. If you print handouts, don’t print this page. (1 of 3)

## Slide 25: Example: Parallel Circuit
Solution:
V
I
R
Current Through Each Component:
Notes: This slide provides the solution. If you print handouts, don’t print this page. (2 of 3)

## Slide 26: Example: Parallel Circuit
Solution:
Verify Kirchhoff’s Current Law:
Notes: This slide provides the solution. If you print handouts, don’t print this page. (3 of 3)

## Slide 27: Summary of Kirchhoff’s Laws
Kirchhoff’s Voltage Law (KVL):
  The sum of all of the voltage drops in a series circuit equals the total applied voltage.
Gustav Kirchhoff
1824-1887
German Physicist
Kirchhoff’s Current Law (KCL):
  The total current in a parallel circuit equals the sum of the individual branch currents.
Notes: Summary of Kirchhoff’s Laws.
http://commons.wikimedia.org/wiki/Image:Gustav_Robert_Kirchhoff.jpg