## Slide 1
AOI Design: Truth Tables to Logic Expressions
© 2014 Project Lead The Way, Inc.
Digital Electronics

## Slide 2: Truth Table & Logic Expressions
This presentation will demonstrate how to…
Properly construct a truth table.
Write a Sum-Of-Products (SOP) logic expression from a truth table.
Create a truth table given a SOP logic expression.
Create a truth table from a set of design specifications (i.e., word problem).
X | Y | OUT
0 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
EQUALS
EQUALS
Design
Specifications
Truth Table
Logic
Expression
Notes: Introductory Slide / Overview of Presentation

## Slide 3: Constructing A Truth Table
A truth table shows how a logic design’s output respond to ALL combinations of possible inputs.
A logic design with N inputs will have 2N input combinations.
The input are listed in binary order (i.e., counting order) in the columns to the left.
The output(s) are listed in the column(s) to the right. (Note some logic circuits can have more than one output.)

## Slide 4: Constructing A Truth Table
X | Y | Z | F1
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Inputs
Output
Input Combinations
  3 – Inputs
  8 – Combinations
  (8 = 23)
Note the binary counting
order of the inputs :
0002 = 010
0012 = 110
0102 = 210
0112 = 310
1002 = 410
1012 = 510
1102 = 610
1112 = 710
Outputs for Each Input Combination
Notes: Example of a three input / one output truth table

## Slide 5: Example Truth Tables
A | B | F2
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
X | Y | Z | F3
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
R | S | T | U | F4
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
3 Inputs
23 = 8 Combinations
4 Inputs
24 = 16 Combinations
2 Inputs
22 = 4 Combinations
Notes: Format for a 2, 3, & 4 variable true table

## Slide 6: Truth Table to Logic Expression
Write the Minterm adjacent to every row in the truth table that contains a one in the output column.
Write the Sum-Of-Products (SOP) logic expression by summing together all of the Minterms.
Example
  Write the SOP logic expression for the output F5 in the truth table below.
X | Y | Z | F5
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Minterms
SOP Logic Expression

## Slide 7: Example #1: Truth Table to Logic Expression
Example
  Write the SOP logic expression for the output F6 in the truth table below.
A | B | C | D | F6
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
Notes: Pause the presentation and allow students to complete the example. The solution is on the next slide.

## Slide 8: Example #1: Truth Table to Logic Expression
Example
  Write the SOP logic expression for the output F6 in the truth table below.
A | B | C | D | F6
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
Solution
Notes: The solution for example #1 is included on this slide. If you print handouts, do not print this page.

## Slide 9: Logic Expression to Truth Table
For each term in the logic expression, place a one in the output column for the input condition that matches the term.
Some terms may match more than one input condition.
Example
  Create the truth table for the following logic expression.
X | Y | Z | F7
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 10: Example #2: Logic Expression to Truth Table
Example
  Create a truth table for the following SOP logic expression.
Notes: Pause the presentation and allow students to complete the example. The solution is on the next slide.

## Slide 11: Example #2: Logic Expression to Truth Table
Example
  Create a truth table for the following SOP logic expression.
A | B | C | D | F8
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0
Solution
Notes: The solution for example #2 is included on this slide. If you print handouts, do not print this page.

## Slide 12: Design Specifications to Truth Table
Identify the number of input variables.
Assign variable names and establish the assignment condition for each variable (i.e., What does a 0 or 1 mean for that input?).
Create a truth table.
Example
  A large fuel tank has sensors that monitor temperature and pressure. Both sensors output a logic LOW if they are within safety range. An alarm will sound if either sensor indicates an unsafe condition is present. Create a truth table for this logic design.
P | T | A
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Assignments :
  P: Pressure Sensor → 0=Safe / 1=Unsafe
  T: Temperature Sensor → 0=Safe / 1=Unsafe
  A: Alarm → 0=Alarm Off / 1=Alarm On

## Slide 13: Example #3: Design Specifications to Truth Table
Example
  Your teacher keeps her final exams in her office. For security reasons, she would like you to design an alarm system for her office. The office has a window and door that are equipped with sensors that output a one when they are secured (i.e., closed). When the alarm system is turned on with a key, the siren should sound if either the window or door is unsecured (i.e., opened).
Notes: Pause the presentation and allow the student to work on the example. The solution is on the next slide.

## Slide 14: Example #3: Design Specifications to Truth Table
Example
  Your teacher keeps her final exams in her office. For security reasons, she would like you to design an alarm system for her office. The office has a window and door that are equipped with sensors that output a one when they are secured (i.e., closed). When the alarm system is turned on with a key, a siren should sound if either the window or door is unsecured (i.e., opened).
K | D | W | S
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Assignments :
  K : Key → 0=System Off / 1=System On
  D : Door Sensor → 0=Open / 1=Closed
  W : Window Sensor → 0=Open / 1=Closed
  S : Siren → 1=On / 0=Off
Solution
Notes: The solution for example #3 is included on this slide. If you print handouts, do not print this page.