## Slide 1
AOI Design: Logic Analysis
© 2014 Project Lead The Way, Inc.
Digital Electronics

## Slide 2: Analysis of Combinational Logic Circuits
Determine the circuit output’s truth-table and logic expression
Determine the circuit’s intended function
Determine whether a circuit is working properly
Did you analyze the circuit BEFORE you turned the power on?
Notes: Introductory Slide / Overview of Presentation
Why is it important to be able to analyze a logic circuit? You may wish to analyze a logic circuit to determine its output’s truth-table and logic expression. You may analyze a previously designed circuit to determine its intended function. Finally, you may need to analyze a circuit that you designed in order to determine whether it works properly.

## Slide 3: Circuit Analysis Techniques
Circuit to Truth Table to Logic Expression
Given a logic circuit . . .
    Extract truth table
    Derive logic expression
Circuit to Logic Expression to Truth Table
Given a logic circuit . . .
    Extract logic expression
    Derive truth table
Notes: Review the two techniques that you can use to analyze a logic circuit.

## Slide 4: Circuit to Truth Table to Logic Expression
The Process
  Add test-points at the output of every gate.
  Add a column to the truth table for every test-point.
  Working from the inputs to the output, complete the truth table for each test-point, ultimately ending at the circuit’s output.
  From the completed truth table, identify the Minterms from the truth table anywhere the output is one.
  Using the extracted Minterms, write the Sum-Of-Products logic expression.
Notes: Review the steps to extract the circuit’s truth table and to determine how to derive the outputs logic expression from it.

## Slide 5: Circuit to Truth Table to Logic Expression
Analyze the logic circuit shown below to determine the circuit’s truth-table. Using the truth table, derive the logic expression for the output F1.
Process Walk-Thru
Notes: Process Walk-Thru on the Truth Table → Equation Process

## Slide 6: Circuit to Truth Table to Logic Expression
Add test-points at the output of every gate.
Process Walk-Thru : Step (a)
TP1
TP2
TP3
TP4
TP5
Notes: Process Walk-Thru on the Truth Table → Equation Process : Step (a)

## Slide 7: Circuit to Truth Table to Logic Expression
Add a column to the truth table for every test-point.
Working from the inputs to the output, complete the truth table for each test-point, ultimately ending at the circuit’s output.
Process Walk-Thru : Steps (b) & (c)
X | Y | Z | F1 | TP1 | TP2 | TP3 | TP4 | TP5
0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
Notes: Process Walk-Thru on the Truth Table → Equation Process : Steps (b) & (c)

## Slide 8: Circuit to Truth Table to Logic Expression
From the completed truth table, identify the Minterms from the truth table anywhere the output is one.
Using the extracted Minterms, write the Sum-Of-Products logic expression.
Process Walk-Thru : Steps (d) & (e)
X | Y | Z | F1 | TP1 | TP2 | TP3 | TP4 | TP5
0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
Notes: Process Walk-Thru on the Truth Table → Equation Process : Steps (d) & (e)

## Slide 9: Example #1: Circuit Analysis
  Analyze the logic circuit shown below to determine the circuit’s truth table. Using the truth table, derive the logic expression for the output F2.
Notes: Pause the presentation and allow students to work on the example. The solution is on the next slide.

## Slide 10: Example #1: Circuit Analysis
Solution
a)
b) & c)
TP1
TP2
TP3
TP4
TP5
e)
A | B | C | F2 | TP1 | TP2 | TP3 | TP4 | TP5
0 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 0
d)
e)
Notes: This is the example #1 solution. If you print handouts, do not print this page.

## Slide 11: Circuit to Logic Expression to Truth Table
  The Process
    Working from the inputs to the output, write the cumulating logic expression at the output of each gate concluding with the expression for the circuit’s output.
    Using the circuit’s output logic expression, derive the circuit’s truth table.
Notes: Review the steps to extract the logic expression for the circuit’s output and how to derive the circuit truth table from it.

## Slide 12: Circuit to Logic Expression to Truth Table
Analyze the logic circuit shown below to determine the logic expression for the output F1. Using the logic expression, derive the circuit’s truth table.
Process Walk-Thru
Notes: Process Walk-Thru on the Equation → Truth Table Process

## Slide 13: Circuit to Logic Expression to Truth Table
Working from the inputs to the output, write the cumulating logic expression at the output of each gate concluding with the expression for the circuit’s output.
Process Walk-Thru : Step (a)
Notes: Process Walk-Thru on the Equation → Truth Table Process : Step (a)

## Slide 14: Circuit to Logic Expression to Truth Table
Using the circuit’s output logic expression, derive the circuit’s truth table.
Process Walk-Thru : Step (b)
X | Y | Z | F1
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Notes: Process Walk-Thru on the Equation → Truth Table Process : Step (b)

## Slide 15: Example #2: Circuit Analysis
  Analyze the logic circuit shown below to determine the logic expression for the output F2. Using the logic expression, derive the circuit’s truth table.
Notes: Pause the presentation and allow students to work on the example. The solution is on the next slide.

## Slide 16: Example #2: Circuit Analysis
A | B | C | F2
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Solution
a)
b)
Notes: This is the example #2 solution. If you print handouts, do not print this page.