## Slide 1
Karnaugh Mapping
© 2014 Project Lead The Way, Inc.
Digital Electronics

## Slide 2: Karnaugh Mapping (K-Mapping)
This presentation will demonstrate how to
Create and label two, three, & four variable K-Maps.
Use the K-Mapping technique to simplify logic designs with two, three, and four variables.
Use the K-Mapping technique to simplify logic design containing don’t care conditions.
Boolean Algebra Simplification
K-Mapping Simplification
≡
Notes: Introductory Slide / Overview of Presentation

## Slide 3: Karnaugh Map Technique
K-Maps are a graphical technique used to simplify a logic equation.
K-Maps are procedural and much cleaner than Boolean simplification.
K-Maps can be used for any number of input variables, BUT are only practical for two, three, and four variables.
Notes: Explain what K-Maps are, why we use them, and the advantages of using K-Maps over Boolean algebra.

## Slide 4: K-Map Format
Each minterm in a truth table corresponds to a cell in the K-Map.
K-Map cells are labeled such that both horizontal and vertical movement differ only by one variable.
Since the adjacent cells differ by only one variable, they can be grouped to create simpler terms in the sum-of-products expression.
The sum-of-products expression for the logic function can be obtained by OR-ing together the cells or group of cells that contain 1s.
Notes: Explain how a K-Map is formatted and how a simplified logic expression can be written from the cell groupings.

## Slide 5: Adjacent Cells = Simplification
 |  | V
 |  | V
 | 1 | 0
 | 1 | 0
 |  | V
 | 1 | 0
 | 1 | 0
Notes: Adjacent cells only vary by one variable change. Review the proof that the one variable changing results in it being eliminated algebraically. This is fundamental to how a K-Map works.

## Slide 6: Truth Table to K-Map Mapping
 |  | V
 | W | X | FWX
Minterm – 0 | 0 | 0 | 1
Minterm – 1 | 0 | 1 | 0
Minterm – 2 | 1 | 0 | 1
Minterm – 3 | 1 | 1 | 0
 |  | V
 | 0 | 1
 | 2 | 3
1
0
1
0
Two Variable K-Map
Notes: Demonstrate how the minterms of a two variable truth table are mapped to a K-Map.

## Slide 7: Two Variable K-Map Groupings
 |  | V
 | 0 | 0
 | 0 | 0
Groups of One – 4
1
1
1
1
Notes: Two variable K-Map, groups of one.

## Slide 8: Two Variable K-Map Groupings
 |  | V
 | 0 | 0
 | 0 | 0
Groups of Two – 4
1
1
1
1
1
1
1
1
Notes: Two variable K-Map, groups of two.

## Slide 9: Two Variable K-Map Groupings
 |  | V
 | 1 | 1
 | 1 | 1
Group of Four – 1
Notes: Two variable K-Map, group of four.

## Slide 10: K-Map Simplification Process
Construct a label for the K-Map. Place 1s in cells corresponding to the 1s in the truth table. Place 0s in the other cells.
Identify and group all isolated 1’s. Isolated 1’s are ones that cannot be grouped with any other one, or can only be grouped with one other adjacent one.
Group any hex.
Group any octet, even if it contains some 1s already grouped but not enclosed in a hex.
Group any quad, even if it contains some 1s already grouped but not enclosed in a hex or octet.
Group any pair, even if it contains some 1s already grouped but not enclosed in a hex, octet, or quad.
OR together all terms to generate the SOP equation.
Notes: Steps for simplifying using the K-Map process.

## Slide 11: Example #1: 2 Variable K-Map
Example:
  After labeling and transferring the truth table data into the K-Map, write the simplified sum-of-products (SOP) logic expression for the logic function F1.
 |  | V
J | K | F1
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
Notes: Pause the presentation and allow the student to complete the example. The solution is on the next slide.

## Slide 12: Example #1: 2 Variable K-Map
Example:
  After labeling and transferring the truth table data into the K-Map, write the simplified sum-of-products (SOP) logic expression for the logic function F1.
 |  | V
 | 1 | 1
 | 0 | 0
Solution:
J | K | F1
0 | 0 | 1
0 | 1 | 1
1 | 0 | 0
1 | 1 | 0
Notes: Here is the solution. If you print handouts, do not print this page.

## Slide 13: Truth Table to K-Map Mapping
 | W | X | Y | FWXY
Minterm – 0 | 0 | 0 | 0 | 1
Minterm – 1 | 0 | 0 | 1 | 0
Minterm – 2 | 0 | 1 | 0 | 0
Minterm – 3 | 0 | 1 | 1 | 0
Minterm – 4 | 1 | 0 | 0 | 0
Minterm – 5 | 1 | 0 | 1 | 1
Minterm – 6 | 1 | 1 | 0 | 1
Minterm – 7 | 1 | 1 | 1 | 0
 |  | V
 | 0 | 1
 | 2 | 3
 | 6 | 7
 | 4 | 5
1
Three Variable K-Map
0
0
0
0
1
1
0
Only one
variable changes
for every row
change
Notes: Demonstrate how the minterms of a three variable truth table are mapped to a K-Map.

## Slide 14: Three Variable K-Map Groupings
 |  | V
 | 0 | 0
 | 0 | 0
 | 0 | 0
 | 0 | 0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
Groups of One – 8 (not shown)
Groups of Two – 12
Notes: Three Variable K-Map:
8 groups of one are not shown because they are obvious.
12 groups of two; all are shown.

## Slide 15: Three Variable K-Map Groupings
Groups of Four – 6
 |  | V
 | 0 | 0
 | 0 | 0
 | 0 | 0
 | 0 | 0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
Notes: Three Variable K-Map:
6 groups of four; all are shown.

## Slide 16: Three Variable K-Map Groupings
Group of Eight - 1
 |  | V
 | 1 | 1
 | 1 | 1
 | 1 | 1
 | 1 | 1
Notes: Three Variable K-Map, Group of Eight.

## Slide 17: Example #2: 3 Variable K-Map
Example:
  After labeling and transferring the truth table data into the K-Map, write the simplified sum-of-products (SOP) logic expression for the logic function F2.
E | F | G | F2
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Notes: Pause the presentation and allow students to complete the example. The solution is on the next slide.

## Slide 18: Example #2: 3 Variable K-Map
Example:
  After labeling and transferring the truth table data into the K-Map, write the simplified sum-of-products (SOP) logic expression for the logic function F2.
 |  | V
 | 0 | 1
 | 1 | 0
 | 1 | 0
 | 0 | 1
Solution:
E | F | G | F2
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 0
Notes: Here is the solution. If you print handouts, do not print this page.

## Slide 19: Truth Table to K-Map Mapping
Four Variable K-Map
 | W | X | Y | Z | FWXYZ
Minterm – 0 | 0 | 0 | 0 | 0 | 0
Minterm – 1 | 0 | 0 | 0 | 1 | 1
Minterm – 2 | 0 | 0 | 1 | 0 | 1
Minterm – 3 | 0 | 0 | 1 | 1 | 0
Minterm – 4 | 0 | 1 | 0 | 0 | 1
Minterm – 5 | 0 | 1 | 0 | 1 | 1
Minterm – 6 | 0 | 1 | 1 | 0 | 0
Minterm – 7 | 0 | 1 | 1 | 1 | 1
Minterm – 8 | 1 | 0 | 0 | 0 | 0
Minterm – 9 | 1 | 0 | 0 | 1 | 0
Minterm – 10 | 1 | 0 | 1 | 0 | 1
Minterm – 11 | 1 | 0 | 1 | 1 | 0
Minterm – 12 | 1 | 1 | 0 | 0 | 1
Minterm – 13 | 1 | 1 | 0 | 1 | 0
Minterm – 14 | 1 | 1 | 1 | 0 | 1
Minterm – 15 | 1 | 1 | 1 | 1 | 1
 |  | V |  | 
 | 0 | 1 | 3 | 2
 | 4 | 5 | 7 | 6
 | 12 | 13 | 15 | 14
 | 8 | 9 | 11 | 10
1
0
1
1
1
1
0
1
0
1
0
0
0
1
1
0
Only one
variable changes
for every row
change
Only one variable changes for every column change
Notes: Demonstrate how the minterms of a four variable truth table are mapped to a K-Map.

## Slide 20: Four Variable K-Map Groupings
 |  | V |  | 
 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0
Groups of One – 16 (not shown)
Groups of Two – 32 (not shown)
Groups of Four – 24 (seven shown)
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
Notes: Four Variable K-Map:
There are 16 groups of one that are not shown because they are obvious.
There are 32 groups of two that are not shown because they are obvious.
There are 24 groups of four. Seven are show, the other 17 are obvious.

## Slide 21: Four Variable K-Map Groupings
 |  | V |  | 
 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0
 | 0 | 0 | 0 | 0
Groups of Eight – 8 (two shown)
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
Notes: Four variable K-Map: There are 8 groups of eight. Two are shown, the other 6 are obvious.

## Slide 22: Four Variable K-Map Groupings
 |  | V |  | 
 | 1 | 1 | 1 | 1
 | 1 | 1 | 1 | 1
 | 1 | 1 | 1 | 1
 | 1 | 1 | 1 | 1
Group of Sixteen – 1
Notes: Four variable K-Map, group of 16.

## Slide 23: Example #3: 4 Variable K-Map
Example:
  After labeling and transferring the truth table data into the K-Map, write the simplified sum-of-products (SOP) logic expression for the logic function F3.
R | S | T | U | F3
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
 |  | V |  | 
Notes: Pause the presentation and allow students to complete the example. The solution is on the next slide.

## Slide 24: Example #3 : 4 Variable K-Map
Example:
  After labeling and transferring the truth-table data into the K-Map, write the simplified sum-of-products (SOP) logic expression for the logic function F3.
Solution:
R | S | T | U | F3
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1
 |  | V |  | 
 | 0 | 1 | 1 | 0
 | 0 | 1 | 1 | 1
 | 1 | 0 | 1 | 1
 | 0 | 1 | 0 | 0
Notes: Here is the solution. If you print handouts, do not print this page.

## Slide 25: Don’t Care Conditions
A don’t care condition, marked by (X) in the truth table, indicates a condition where the design doesn’t care if the output is a (0) or a (1).
A don’t care condition can be treated as a (0) or a (1) in a K-Map.
Treating a don’t care as a (0) means that you do not need to group it.
Treating a don’t care as a (1) allows you to make a grouping larger, resulting in a simpler term in the SOP equation.

## Slide 26: Some You Group, Some You Don’t
 |  | V
 | X | 0
 | 1 | 0
 | 0 | 0
 | X | 0
This don’t care condition was treated as a (1). This allowed the grouping of a single one to become a grouping of two, resulting in a simpler term.
There was no advantage in treating this don’t care condition as a (1), thus it was treated as a (0) and not grouped.
Notes: Explain that you include don’t care conditions only if it allows you to make a grouping larger.

## Slide 27: Example #4: Don’t Care Conditions
Example:
  After labeling and transferring the truth table data into the K-Map, write the simplified sum-of-products (SOP) logic expression for the logic function F4. Be sure to take advantage of the don’t care conditions.
R | S | T | U | F4
0 | 0 | 0 | 0 | X
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | X
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | X
0 | 1 | 1 | 0 | X
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | X
1 | 1 | 0 | 0 | X
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0
 |  | V |  | 
Notes: Pause the presentation and allow students to complete the example. The solution is on the next slide.

## Slide 28: Example #4: Don’t Care Conditions
Example:
  After labeling and transferring the truth table data into the K-Map, write the simplified sum-of-products (SOP) logic expression for the logic function F4. Be sure to take advantage of the don’t care conditions.
Solution:
R | S | T | U | F4
0 | 0 | 0 | 0 | X
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | X
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | X
0 | 1 | 1 | 0 | X
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | X
1 | 1 | 0 | 0 | X
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0
 |  | V |  | 
 | X | 0 | X | 1
 | 0 | X | 1 | X
 | X | 0 | 0 | 0
 | 1 | 1 | X | 1
Notes: Here is the solution. If you print handouts, do not print this page.