## Slide 1
Universal Gate – NAND
Digital Electronics

## Slide 2: Universal Gate – NAND
This presentation will demonstrate
The basic function of the NAND gate.
How a NAND gate can be used to replace an AND gate, an OR gate, or an INVERTER gate.
How a logic circuit implemented with AOI logic gates can be re-implemented using only NAND gates.
That using a single gate type, in this case NAND, will reduce the number of integrated circuits (IC) required to implement a logic circuit.
AOI Logic
NAND Logic
More ICs = More $$
Less ICs = Less $$
Notes: Introductory Slide / Overview of Presentation

## Slide 3: NAND Gate
X | Y | Z
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
X
Y
Notes: Overview of basic NAND gate : Logic Symbol, Logic Expression (using DeMorgan’s) and Truth Table.

## Slide 4: NAND Gate as an Inverter Gate
X | Z
0 | 1
1 | 0
X
(Before Bubble)
Equivalent to Inverter
Notes: When you tie the inputs on a NAND gate together, the output will be the complement of the input.

## Slide 5: NAND Gate as an AND Gate
X | Y | Z
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
X
Y
NAND Gate
Inverter
Equivalent to AND Gate
Notes: This one is easy to see, a NAND gate is an AND gate with the output inverted. So if you invert the output again, you will get an AND gate. Note that we are using a NAND gate for the inverter.

## Slide 6: NAND Gate as an OR Gate
X | Y | Z
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Equivalent to OR Gate
X
Y
NAND Gate
Inverters
Notes: This one is a bit harder to see. If you invert both of the inputs of a NAND gate, you will get an OR gate. Note that we’re using NAND gates as inverters.

## Slide 7: NAND Gate Equivalent to AOI Gates
INVERTER
OR
AND
Notes: Summary of the three AOI gates and their NAND equivalent.

## Slide 8: Process for NAND Implementation
If starting from a logic expression, implement the design with AOI logic.
In the AOI implementation, identify and replace every AND,OR, and INVERTER gate with its NAND equivalent.
Redraw the circuit.
Identify and eliminate any double inversions (i.e., back-to-back inverters).
Redraw the final circuit.
Notes: Process for implementing NAND only circuits from AOI.

## Slide 9: NAND Implementation
Example:
  Design a NAND Logic Circuit that is equivalent to the AOI circuit shown below.
Notes: Example

## Slide 10: NAND Implementation
Solution – Step 2
Identify and replace every AND,OR, and INVERTER gate with its NAND equivalent.
Notes: Example : Solution Step 2 (Note that there wasn’t a step 1 because we started with an AOI circuit.)

## Slide 11: NAND Implementation
Redraw the circuit.
Solution – Step 3
Notes: Example : Solution Step 3

## Slide 12: NAND Implementation
Identify and eliminate any double inversions.
Solution – Step 4
Notes: Example : Solution Step 4

## Slide 13: NAND Implementation
Solution – Step 5
Redraw the circuit.
Notes: Example : Solution Step 5

## Slide 14: Proof of Equivalence
Notes: Algebraic proof that the NAND only circuit is equivalent to the AOI.

## Slide 15: AOI vs. NAND
IC Type | Gates | Gate / IC | # ICs
74LS04 | 1 | 6 | 1
74LS08 | 2 | 4 | 1
74LS32 | 1 | 4 | 1
Total Number of ICs → |  |  | 3
IC Type | Gates | Gate / IC | # ICs
74LS00 | 4 | 4 | 1
Total Number of ICs → |  |  | 1
Notes: Comparison of the two implementations. Note the reduced IC count (3 to 1), which would result in a cost savings.