## Slide 1
Octal and Hexadecimal
Number Systems
Digital Electronics
Notes: Introductory Slide / Overview of Presentation

## Slide 2: What, More Number Systems?
Why do we need more number systems?
  Humans understand decimal
  Digital electronics (computers) understand binary
  Since computers have 32, 64, and even 128 bit busses, displaying numbers in binary is cumbersome.
  Data on a 32 bit data bus would look like the following:
  0110 1001 0111 0001 0011 0100 1100 1010
  Hexadecimal (base 16) and octal (base 8) number systems are used to represent binary data in a more compact form.
  This presentation will present an overview of the process for converting numbers between the decimal number system and the hexadecimal & octal number systems.
Check out my ten digits !
Notes: In general, a bus is a common ire or parallel group of wires connecting multiple circuits. A data bus is a way of transferring data within and outside a computer.

## Slide 3: Converting To and From Decimal
Successive
Division
Weighted
Multiplication
Octal8
0 1 2 3 4 5 6 7
Successive
Division
Hexadecimal16
0 1 2 3 4 5 6 7 8 9 A B C D E F
Weighted
Multiplication
Successive
Division
Weighted
Multiplication
Binary2
0 1
Decimal10
0 1 2 3 4 5 6 7 8 9
Notes: This slide first presents a graphical overview of the process for converting between DECIMAL↔BINARY (students should know how to do this) and then generalizes this process for converting between DECIMAL↔OCTAL & DECIMAL↔HEXADECIMAL.

## Slide 4: Counting . . . 2, 8, 10, 16
Decimal |  | Binary |  | Octal |  | Hexadecimal
0 |  | 00000 |  | 0 |  | 0
1 |  | 00001 |  | 1 |  | 1
2 |  | 00010 |  | 2 |  | 2
3 |  | 00011 |  | 3 |  | 3
4 |  | 00100 |  | 4 |  | 4
5 |  | 00101 |  | 5 |  | 5
6 |  | 00110 |  | 6 |  | 6
7 |  | 00111 |  | 7 |  | 7
8 |  | 01000 |  | 10 |  | 8
9 |  | 01001 |  | 11 |  | 9
10 |  | 01010 |  | 12 |  | A
11 |  | 01011 |  | 13 |  | B
12 |  | 01100 |  | 14 |  | C
13 |  | 01101 |  | 15 |  | D
14 |  | 01110 |  | 16 |  | E
15 |  | 01111 |  | 17 |  | F
16 |  | 10000 |  | 20 |  | 10
17 |  | 10001 |  | 21 |  | 11
18 |  | 10010 |  | 22 |  | 12
19 |  | 10011 |  | 23 |  | 13
Notes: This slide lists the first twenty numbers in each of the four number systems (decimal, binary, octal, hexadecimal).
This is the first time that students will have see A, B, C, D, E, & F used in a “number” system. Remember from Unit 1 that a number system uses its number of symbols to designate values. Base 16 needs 16 unique symbols; 10 is not a unique symbol, it is two. Therefore, the letter A is used to stand for 10, B for 11, and so on.

## Slide 5: Review: Decimal ↔ Binary
Base10
DECIMAL
Base2
BINARY
Successive
Division
  Divide the decimal number by 2; the remainder is the LSB of the binary number.
  If the quotation is zero, the conversion is complete. Otherwise repeat step (a) using the quotation as the decimal number. The new remainder is the next most significant bit of the binary number.
  Multiply each bit of the binary number by its corresponding bit-weighting factor (i.e., Bit-0→20=1; Bit-1→21=2; Bit-2→22=4; etc).
  Sum up all of the products in step (a) to get the decimal number.
Weighted
Multiplication
Base10
DECIMAL
Base2
BINARY
Notes: Review the process for DECIMAL-to-BINARY and BINARY-to-DECIMAL.

## Slide 6: Conversion Process Decimal ↔ BaseN (Any base including Binary2, Octal8, Hexidecimal16)
Base10
DECIMAL
BaseN
ANY BASE
Successive
Division
  Divide the decimal number by N; the remainder is the LSB of the ANY BASE Number .
  If the quotient is zero, the conversion is complete. Otherwise repeat step (a) using the quotient as the decimal number. The new remainder is the next most significant bit of the ANY BASE number.
  Multiply each bit of the ANY BASE number by its corresponding bit-weighting factor (i.e., Bit-0→N0; Bit-1→N1; Bit-2→N2; etc).
  Sum up all of the products in step (a) to get the decimal number.
Weighted
Multiplication
Base10
DECIMAL
BaseN
ANY BASE
Notes: Relate that successive division and the weighted multiplication process used for Decimal ↔ Binary conversion can be used for ANY base.

## Slide 7: Decimal ↔ Octal Conversion
  The Process: Successive Division
  Divide the decimal number by 8; the remainder is the LSB of the octal number .
  If the quotation is zero, the conversion is complete. Otherwise repeat step (a) using the quotation as the decimal number. The new remainder is the next most significant bit of the octal number.
  Example:
  Convert the decimal number 9410 into its octal equivalent.
 9410 = 1368
Notes: Review the DECIMAL-to-OCTAL conversion process.
Remind students to subscript all numbers (i.e., Subscript 10 for decimal & subscript 8 for octal).

## Slide 8: Example: Decimal → Octal
Example:
  Convert the decimal number 18910 into its octal equivalent.
Notes: Pause the presentation and allow students to complete the example. The solution is on the next slide.

## Slide 9: Example: Decimal → Octal
Example:
  Convert the decimal number 18910 into its octal equivalent.
Solution:
 18910 = 2758
Notes: Here is the solution. If you print handouts, do not print this page.

## Slide 10: Octal ↔ Decimal Process
  The Process: Weighted Multiplication
  Multiply each bit of the Octal Number by its corresponding bit-weighting factor (i.e., Bit-0→80=1; Bit-1→81=8; Bit-2→82=64; etc.).
  Sum up all of the products in step (a) to get the decimal number.
  Example:
  Convert the octal number 1368 into its decimal equivalent.
 136 8 = 9410
1 |  | 3 |  | 6 |  | 
82 |  | 81 |  | 80 |  | 
64 |  | 8 |  | 1 |  | 
64 | + | 24 | + | 6 | = | 9410
Bit-Weighting
Factors
Notes: Review the OCTAL-to-DECIMAL conversion process.
Let the students know that as the become more proficient at the conversions, they may not need to write out the Bit-Weighting Factors.

## Slide 11: Example: Octal → Dec
Example:
  Convert the octal number 1348 into its decimal equivalent.
Notes: Pause the power point and allow the student to work on the example. The solution is on the next slide.

## Slide 12: Example: Octal → Decimal
Example:
  Convert the octal number 1348 into its decimal equivalent.
1348 = 9210
1 |  | 3 |  | 4 |  | 
82 |  | 81 |  | 80 |  | 
64 |  | 8 |  | 1 |  | 
64 | + | 24 | + | 4 | = | 9210
Solution:
Notes: Here is the solution. If you print handouts, don’t print this page.

## Slide 13: Decimal ↔ Hexadecimal Conversion
  The Process: Successive Division
  Divide the decimal number by 16; the remainder is the LSB of the hexadecimal number.
  If the quotation is zero, the conversion is complete. Otherwise repeat step (a) using the quotation as the decimal number. The new remainder is the next most significant bit of the hexadecimal number.
  Example:
  Convert the decimal number 9410 into its hexadecimal equivalent.
 9410 = 5E16
Notes: Review the DECIMAL-to-HEXADECIMAL conversion process.
Note the subscript notation of (16) and (H) are both acceptable for hexadecimal numbers.

## Slide 14: Example: Decimal → Hex
Example:
  Convert the decimal number 42910 into its hexadecimal equivalent.
Notes: Pause the power point and allow the student to work on the example. The solution is on the next slide.

## Slide 15: Example: Decimal → Hexadecimal
Example:
  Convert the decimal number 42910 into its hexadecimal equivalent.
Solution:
 42910 = 1AD16 = 1ADH
Notes: Here is the solution. If you print handouts, do not print this page.

## Slide 16: Hexadecimal ↔ Decimal Process
  The Process: Weighted Multiplication
  Multiply each bit of the hexadecimal number by its corresponding bit-weighting factor (i.e., Bit-0→160=1; Bit-1→161=16; Bit-2→162=256; etc.).
  Sum up all of the products in step (a) to get the decimal number.
  Example:
  Convert the octal number 5E16 into its decimal equivalent.
 5E 16 = 9410
5 |  | E |  | 
161 |  | 160 |  | 
16 |  | 1 |  | 
80 | + | 14 | = | 9410
Bit-Weighting
Factors
Notes: Review the HEXADECIMAL-to-DECIMAL conversion process.
Let the students know that as they become more proficient at the conversions, they may not need to write out the Bit-Weighting Factors.

## Slide 17: Example: Hexadecimal → Decimal
Example:
  Convert the hexadecimal number B2EH into its decimal equivalent.
Notes: Pause the presentation and allow students to work on the example. The solution is on the next slide.

## Slide 18: Example: Hexadecimal → Decimal
Example:
  Convert the hexadecimal number B2EH into its decimal equivalent.
B2EH = 286210
B |  | 2 |  | E |  | 
162 |  | 161 |  | 160 |  | 
256 |  | 16 |  | 1 |  | 
2816 | + | 32 | + | 14 | = | 286210
Solution:
Notes: Here is the solution. If you print handouts, do not print this page.

## Slide 19: Example: Hexadecimal → Octal
Example:
  Convert the hexadecimal number 5AH into its octal equivalent.
Notes: Pause the presentation and allow students to work on the example. The solution is on the next slide.
For this example, the students will need to realize that they must first convert from HEXADECIMAL-to-DECIMAL then DECIMAL-to-OCTAL. Let them think about it a little before telling them this extra step.

## Slide 20: Example: Hexadecimal → Octal
Example:
  Convert the hexadecimal number 5AH into its octal equivalent.
5AH = 1328
5 |  | A |  | 
161 |  | 160 |  | 
16 |  | 1 |  | 
80 | + | 10 | = | 9010
Solution:
  First convert the hexadecimal number into its decimal equivalent, then convert the decimal number into its octal equivalent.
Notes: Here is the solution. If you print handouts, do not print this page.

## Slide 21: Example: Octal → Binary
Example:
  Convert the octal number 1328 into its binary equivalent.
Notes: Pause the presentation and allow students to work on the example. The solution is on the next slide.
For this example, the students will realize that they must first convert from OCTAL-to-DECIMAL, then DECIMAL-to-BINARY. Let them think about it a little before telling them this extra step.

## Slide 22: Example: Octal → Binary
Example:
  Convert the octal number 1328 into its binary equivalent.
1328 = 10110102
1 |  | 3 |  | 2 |  | 
82 |  | 81 |  | 80 |  | 
64 |  | 8 |  | 1 |  | 
64 | + | 24 | + | 2 | = | 9010
Solution:
  First convert the octal number into its decimal equivalent, then convert the decimal number into its binary equivalent.
Notes: Here is the solution. If you print handouts, don’t print this page.

## Slide 23: Binary ↔ Octal ↔ Hex Shortcut
Because binary, octal, and hex number systems are all powers of two (which is the reason we use them) there is a relationship that we can exploit to make conversion easier.
To convert directly between binary and octal, group the binary bits into sets of 3 (because 23 = 8). You may need to pad with leading zeros.
To convert directly between binary and hexadecimal number systems, group the binary bits into sets of 4 (because 24 = 16). You may need to pad with leading zeros.
1 0 1 1 0 1 0 2 = 132 8 = 5A H
0 0 1 0 1 1 0 1 0 2 = 1 3 2 8
1 3 2 0 0 1 0 1 1 0 1 0
0 1 0 1 1 0 1 0 2 = 5 A 16
5 A 0 1 0 1 1 0 1 0
Notes: This shortcut is VERY useful, but it will only work with the number systems bases that are powers of (2).

## Slide 24: Example: Binary ↔ Octal ↔ Hex
Example:
  Using the shortcut technique, convert the hexadecimal number A616 into its binary and octal equivalent. Use your calculator to check your answers.
Notes: Pause the presentation and allow students to complete the example. The solution is on the next slide.

## Slide 25: Example: Binary ↔ Octal ↔ Hex
Solution:
  First convert the hexadecimal number into binary by expanding the hexadecimal digits into binary groups of (4).
  Convert the binary number into octal by grouping the binary bits into groups of (3).
0 1 0 1 0 0 1 1 0
2 4 6
A 6 16
1 0 1 0 0 1 1 0
101001102 = 2468
A616 = 101001102
Example:
  Using the shortcut technique, convert the hexadecimal number A616 into its binary & octal equivalent. Use your calculator to check your answers.
Notes: Here is the solution. If you print handouts, do not print this page.