## Slide 1
Flip-Flop Applications
Digital Electronics

## Slide 2: Flip-Flop Applications
This presentation will provide an overview of the following flip-flop applications:
  Event Detect
  Data Synchronizer
  Shift Register
  Frequency Divider
Additional flip-flop applications will be covered in future lessons:
  Asynchronous {Ripple} Counters
  Synchronous {Parallel} Counters
  State Machines
Notes: Introductory Slide / Overview of Presentation

## Slide 3: Event Detector
An event detector circuit is one that is capable of detecting and holding a signal until the event that changed the signal can be addressed.
For example, door sensors on a home burglar alarm system use an event detector circuit. Once someone opens the door, the alarm will sound until the system is turned off.
If it were not for the event detection circuit, the alarm would only be on when the door was open. Thus, someone could quickly open the door, enter the house, and close the door. In this situation the alarm would only sound for the brief time that the door was actually open.
Notes: Description of what an event detector circuit is used for. Ask the students to think of other applications.

## Slide 4: Event Detect: Circuit
Notes: Event detector circuit with a D flip-flop.

## Slide 5: Event Detect
Single_Event
Clear
Held_Event
Single_Event
Clear
Held_Event
Event
Held
Event
Cleared
Multiple Events
Only the 1st event is held.
Multiple Clears
Only the 1st event does anything.
Case #1
Case #2
Notes: Simulation of the Event Detector circuit.
The top timing diagram (Case #1) shows that when the Single_Event signal changes (0-to-1), the event is held by the output signal Held_Event until it is cleared.
The bottom timing diagram (Case #2) shows that when multiple events occur, only the first is held. The same is true with multiple clears.

## Slide 6: Data Synchronizer
Normally, timing is not a concern with combinational logic. However, due to gate delays, the outputs of combinational logic can change at different times. This can lead to potential timing problems. Take a look at the combinational logic circuit shown below. Because functions A, B, & C have different circuit complexity, they change logic levels at different times.
To solve this problem, a data synchronizer circuit can be added to the outputs.
C |  |  |  |  |  |  |  |  |  |  | 
B |  |  |  |  |  |  |  |  |  |  | 
A |  |  |  |  |  |  |  |  |  |  | 
Combinational
Logic
Circuit
.
.
.
Inputs
Notes: Description of what a data synchronizer circuit is used for.

## Slide 7: Data Synchronizer: Circuit
Notes: Data synchronizer circuit with a D flip-flop.

## Slide 8: Data Synchronizer: Timing
Latched_A |  |  |  |  |  |  |  |  | 
Latched_B |  |  |  |  |  |  |  |  | 
Latched_C |  |  |  |  |  |  |  |  | 
A |  |  |  |  |  |  |  |  | 
B |  |  |  |  |  |  |  |  | 
C |  |  |  |  |  |  |  |  | 
Clock |  |  |  |  |  |  |  |  | 
 | The signal can be a zero or a one, depending on the previous latched values. |  |  |  |  |  |  |  | 
Notes: Timing diagram for the data synchronizer circuit.

## Slide 9: Frequency Divider
As the name implies, a frequency divider is a circuit the produces a digital output signal that is half the frequency of the input.
The frequency divider is used extensively in the design of asynchronous counters.
Notes: Description of what a data synchronizer circuit is used for.

## Slide 10: Frequency Divider: Circuit
Clock_Out
Clock_In
D Version
J/K Version
Notes: Timing diagram for the frequency divider (divide-by-two circuit). Note that this circuit can be implemented with both the D and J/K flip-flops.

## Slide 11: Frequency Divider: Timing
Clock_Out
Clock_In
T1
T2
The period of Clock_Out is twice the period of Clock_In.
Since the period is twice, the frequency is divided in half.
Notes: Detailed view of the period and frequency of the input/output signals for the divide-by-two circuit.

## Slide 12: Shift Register
A shift register is a group of flip-flops (typically 4 or 8) that are arranged so that the values stored in the flip-flops are shifted from one flip-flop to the next for every clock.
Shift registers are used extensively in logic circuits to control digital displays.
A classic example is numbers being typed into a calculator. As the numbers are entered, the digits shift to the left one position. This shifting is controlled by a shift register.
Notes: Description of what a shift register circuit is used for. Ask the students to think of other applications.

## Slide 13: Shift Register
Data In
Data Out
Data Out
Data In
Data Out
Data In
Data Out
Data In
Serial In / Serial Out
Left-to-Right
Serial In / Serial Out
Right-to-Left
Serial In / Parallel Out
Parallel In / Serial Out
Notes: The four most common types of shift registers. Some textbooks also discuss the parallel in / parallel out shift register.

## Slide 14: Shift Register: Circuit (D)
Notes: A Serial In / Parallel Out shift register with D flip-flops.

## Slide 15: Shift Register: Circuit (J/K)
Notes: A Serial In / Parallel Out shift register with J/K flip-flops.

## Slide 16: Shift Register: Timing
Clock
Data_In
D1
D2
D3
D4
Notes: Time diagram for the proceeding Serial In / Parallel Out shift registers.

## Slide 17: MSI Shift Register
74LS194 (4-bit Bi-Directional Universal Shift Register)
Parallel Inputs
Serial Inputs
Mode Control
Parallel Outputs
&
Serial Outputs
Clear & Clock
Notes: Overview of commonly used MSI Shift Registers. This IC is very common because is can be used to implement a
Serial In / Serial Out, a Parallel In / Serial Out, and Serial In / Parallel Out shift register.

## Slide 18: 74LS194 Shift Register: Circuit
Notes: Design example of a In / Parallel Out shift register using a 74LS194 IC.

## Slide 19: 74LS194 Shift Register: Timing
Clock
X4
X3
X2
X1
Data_In
Notes: Time diagram for the preceding Serial In / Parallel Out shift register.